6. oktober 2014

Quantum monte carlo

The system:
Electrons in a harmonic oscillator trap.

The physics of the system:
N=2 electrons
(later, 6 and 12)
confined to move in a harmonic oscillator trap.

psi(r1,o1,r2,o2) = R(r1,r2) X(o1,o2)	[o – sigma]

Antisymmetric wavefunction (fermions)

Harmonic oscillator:
one particle in two dimensions has an energy:
Cartesian coordinates:
E_nx,ny = hbar omega (nx + ny + 1)
Single electron wave-function:
psi(x,y) = H_nx(x) H_ny(y)	[H hermite polynomials]

Spherical coordinates:
E_n,ml = hbar omega (2n + |ml| + 1)

3 dimensions:
Cartesian coordinates:
E_nx,ny,nz = hbar omega(nx + ny + nz + 3/2)

Degeneracy:
No repulsion, the two electron energies in the lowest state:
2 hbar omega First test of the system, first benchmark
Ansatz for the ground state:
psi(r1,o1,r2,o2)
The spin must be zero(antisymmetric)
The Hamiltonian doesn't affect the spin part.
= psi(r1,r2) X(o1,o2)
R propto phi_nx1,ny1(x1 y1) phi_nx2,ny2 (x2 y2)
Ground state: nx1 = ny1 = nx2 = ny2 = 0
H_0(x) = N e^(-x^2/2) [hbar omega = 1]
R propto e^(-x1² + y1² + x2² + y2²)/2 = e^(r1²+r2²)/2

Variational principle:
H psi = E psi
phi0 = sumi Ci psi
<phi0 | H | psi0>/
<psi0 | psi0>
= sumi E_i |Ci|² /sumi |Ci|²
E0 < E1 < E2 < …

If phi0 = psi0
<H> = E0	[obviously]

the general case is not:
<H> \geq E0	[The variational principle]

The variance of the energy:
< H² > - <H>² = 0 iff. We have the exact solution.

We're going to have:

i)
A trial wave function which depends on some parameters which we are going to vary.
psi_T(R,alpha)	[alpha – parameter]

ii)
Compute
E(alpha) = <psi_T | H | psi_T>/<psi_T | psi_T>

iii)
Find the minimum of E(alpha)
Plot E(alpha) against alpha.
Plot var(E)

For the N=2 ansatz:
psi_T (r1,r2,alpha) = e^-alpha(r1² + r2²)/2

The integral:
E(alpha) = int d tau (psi_T(tau,alpha) H psi_T(tau, alpha))/norm
We'll use the metropolis algorithml
avoids the calculation of the norm
<E(alpha)> = int d tau P(tau,alpha) E_L (alpha)

Quantum mechanics:
P(tau, alpha) = |psi_T(tau,alpha)|²/ int(|psi_T (tau,alpha)|²)

E_L = 1/psi_T H psi_T(tau,alpha)
=>
<E(alpha)> = int dtau P(tau,alpha) E_L(alpha)